VP 44 pumps – REPAIRS

This text write in order to help in practical work vp 44 stations. I rely on experience, and is intended for beginners masters.

In previous work we met with failures of pumps that globally can be divided into three groups

1 Failures electronics pumps that take 60-70% of  all failures

2 Failures mechanical pump which consumes about 25% of total failures

3 Leaks ie faults in the sealing of the pump which consumes about 15% of total failures electronics failure

Failures electronics

We note the diagnostic device. mostly it is a mistake   "Fuel valve" refers to the upper valve is located between the Pipe nozzles. This  pump have not fuelt and the car will not start. On the workbench, the pump response. Correctly adjust start injection show temperature and RPM , but not have injection on injectors. The fault is MOSFET transistor driver  valve to adj. fuel. Transistor can  replace,  use the transistor IRLR2905 or better IRLR 3110 see next picture

Electronics repair pumps - Replacing MOSFET transistor (driver valve for adj. fuel)

You must use IRLR 2905 or 3110. Not use IRFZ 44

Another defect that we can answer in practice is an error in the CAN communication . Communication is broken and pump  not respond wih test bench. All is same as pump not present. Usually damaged Mosfet Transistor causes and this damage.. The fault is 5V voltage regulator that can successfully replace. We use a stabilizer 7805 or better 78S05 Replacement stabilizer

- gnd

- 12v

- 5v

7805

3. defect when Car diagnostic  not the correctness of speed sensor on the test bench, the pump response can adjust the amount and angle. When you rotate the pump it displays the temperature does not show the speed  and not have injection. If the pump is on the car, the car will not start. Error is sensor of position rotor (RPM sensor),

Same symptom may have and lost capatitor (lost solder not have good contact)

Usualy when capatitor is lost pump work correctly few minutes.

Look in next picture

NECESSARY TOOL FOR REPAIR ELECTRIC PUMPS

1 table pounding that increases 3-4 times

2 soldering iron with temperature control

3 quality tweezers

4 standard tool pliers

MATERIALS NEEDED FOR REPAIR ELECTRIC PUMPS

1 MOSFET Transistor IRLR 2905 or 3110 ILRL both smd

2 voltage regulator 5V 7805 or 78S05 - TO220

3 Solder wires  1mm

4 Liquid flux - the means to act coagulation (for better soldering)

5 mica insulators for housing TO220 (good dielectric )

6 Silicone pasta (for better cooling)

.

DAMAGE MECHANICS OF PUMPS

Mechanical failures can be very diverse, but in practice usually have same defect.

When car start, and have  smoke is usually white smoke Diagnostic device errors occur "start  injection," with Car diagnostic reads the  parameters angle of start injection not good.Error repair following order.  Visual inspection, measurement of pressure, angle of injection test. Repairing or replacing is not the correct part At the end of the test on work bench of the angle of injection

DESCRIPTION

Pump cleaned and put on workbench. Cut one wire from the bottom valve, adjust the amount of fuel at around 2500, and turn the pump on the 100 RPM first and y increase the speed to 400 RPM Stroboscope follow the angle of the pump to around 100 Nominal angle is zero and gradually increases to 12 -16 degrees. If we have not described this result we confirmed the foult. Next a test is a test which transfers the pressure to be 9 bars min at 400 rpm  If he's wrong mistake in the fuel supply or transver pump (usually it's all ok) In the next measurement is necessary to remove the bottom valve (for start injection), and in its place transver measured pressure at 400 rpm must be 9-18 bar .. if you do not have that kind of pressure fault in the pump housing so. Small nozzle repair picture look:

Drill hole 4mm on place (ode busiti) and use long needle for remove nozzle

If the pressure is OK must inspection of stop valve look piture:

Usuali damage bootom rubber on picture brown

And next inspection is clip look next picture

Repair damage polishing

Inspection and

If  Hole of clip not good usually can repair this polishing

Tools Required

1 Diesel stroboscope

2 barometric instrument measuring pressure transver

3 tools for outbreak clip

4 tool for extracting bearings

5 standard tool for disassembly

MATERIALS NEEDED

1 Set for sealing pumps

2 clip with carabiner clip (mostly successfully improves processing)

Conclusion: if you have all the necessary tools with a little practice and accuracy is not a problem to fix the mechanics of the pump

DAMAGE sealing PUMPS Failures sealing pumps mainly occurs during the winter. Car will not start in the morning. When is start engine work all day.

Usually damage screws (bolts) to block the pump (rubber), rubber electronic pump (located under electronics)

Date: 22.03.2013

Nikola Bogdan

Autoelektronika Sombor

web: www.autoelektronika .co.rs